## Slide 1: LLM-Guided Search for Optimal AllToAllV on AWS Trainium
Combining Claude, Genetic Algorithms, and Contention-Guided Synthesis

## Slide 2: Why AllToAllV Matters
Mixture-of-Experts (MoE) training
- Tokens routed to specialized experts across ranks
- AllToAllV: variable-length all-to-all = core MoE primitive
- Called 4x per MoE layer per training step
On AWS Trainium
- Must build from XLA primitives (all_gather, collective_permute)
- No NCCL; default approaches are slow
- Multi-node (EFA) adds cross-node overhead

## Slide 3: Trainium trn1.32xlarge
Intra-node topology
- 16 NeuronDevices in 4x4 2D torus, 2 cores each (32 ranks)
- NeuronLink: ~192 GB/s per link, 4 links per device
- Max 4 hops, avg 2 hops across torus
Inter-node (EFA)
- 8 EFA adapters/node @ 12.5 GB/s each
- 2-node cluster: 64 ranks, 32 devices, NeuronLink + EFA
XLA collective primitives
- all_gather: broadcast, single dispatch, HW-optimized
- collective_permute: point-to-point, one dispatch per distance
- all_to_all: XLA decomposes to internal ring (deceptively slow)

## Slide 4: Key Insight: Dispatch Overhead Dominates
Each XLA op costs ~0.03 ms fixed dispatch overhead
- Bandwidth (192 GB/s) is never the bottleneck
- Latency is flat from 32 KB to 512 MB
Naive AllGather: 33 XLA ops = ~1.05 ms
Default Ring: 93 XLA ops = ~2.78 ms
Optimized (agent output): 3 XLA ops = ~0.13 ms
Reducing XLA IR node count is the only lever

## Slide 5: Search Pipeline: 5 Phases + Feedback Loops
Phase 1: Agent hardware profiling (LLM builds simulator)
- Discovers topology, overheads; writes cost model; validates <20% error
Phase 2: Baseline eval on simulator -> knowledgebase
- All templates + GA/SA refinement + LLM candidates
Phase 3: Multi-island evolution with simulator feedback
- 3 islands + CGIS + template evolution (XLA + NKI)
Phase 4: Iterative mini-benchmarking on real HW
- Compare HW vs sim; refine simulator if predictions diverge
Phase 5: Final code generation -> trainium_alltoallv.py
Feedback: Phase 2/3 return to Phase 1 to refine simulator

## Slide 6: Topology Simulator
Models the 4x4 NeuronLink torus
- Per-link bandwidth, latency, hop counts
- Simulates 6 algorithm templates
Multi-objective cost function
- sim_time + dispatch penalty + hop cost + contention
Limitation: underweights dispatch overhead
- Ranked 2-gather above 1-gather; hardware shows opposite
- Simulation prunes bad candidates; hardware decides final rank

## Slide 7: CGIS: Contention-Guided Iterative Synthesis
Traditional: LLM -> schedule -> score -> LLM (blind)
CGIS: LLM -> schedule -> contention diagnosis -> LLM
- "Step 5 saturated link (4,8) at 6x. Separate distances 8 and 24."
- LLM makes surgical fix instead of blind mutation
Three components
- ContentionAnalyzer: per-link conflict detection
- IterativeRefinement: multi-turn LLM + contention feedback
- IslandEvolution: 3 islands with LLM crossover

## Slide 8: Template Evolution: Dual-Backend
Beyond parameter tuning: LLM generates complete Python code
XLA path (default)
- Seeds: naive_allgather, allgather_reduce_scatter
- TrackedTensor counts XLA IR ops; CollectiveSimulator tests correctness
- LLM discovers how to reduce 67 ops -> 4 ops
NKI path (research)
- Seeds: nki_naive_allgather, nki_permute_ring
- NKI collectives have ~7x higher dispatch than XLA on trn1
5-layer correctness verification for both backends

## Slide 9: Search Convergence (MoE Traffic)
From allgather seed
- 3 rounds, no improvement (already optimal at 493 us)
From hierarchical seed
- Baseline: 3615 us (31 collective_permute ops)
- Round 1: 493 us -- switched to AllGather pattern (86% improvement)
- Round 2: 249 us -- 2-phase subgroup AllGather (50% further)
From permute_ring seed
- Round 1: 493 us -- switched to AllGather (86% improvement)
- Round 2: failed (tensor shape mismatch)

## Slide 10: Agent Output: AllGather + index_select
Algorithm (~3 XLA IR ops total)
- Pad send buffer to uniform size
- Single all_gather: collect all ranks' buffers
- Single index_select: extract needed elements via flat index
On XLA devices
- All Python ops trace into HLO at compile time
- Flat index = compile-time constant, zero runtime overhead
- ~0.13 ms on trn1.32xlarge

## Slide 11: Single-Node Benchmark (32 ranks, NeuronLink)
Algorithm | Type | 32KB | 128KB | 512KB | 2MB | 8MB
Agent Output | agent | 0.127 | 0.136 | 0.132 | 0.123 | 0.127
AG+ReduceScatter | baseline | 0.719 | 0.727 | 0.729 | 0.739 | 0.729
NKI AllGather | baseline | 0.865 | 0.894 | 0.909 | 0.869 | 0.877
AllGather+Slice | baseline | 1.035 | 1.890 | 1.061 | 1.046 | 1.060
Fused AllToAll | baseline | 2.257 | 1.195 | 1.195 | 1.196 | 1.202
Hierarchical | baseline | 2.869 | 2.205 | 2.235 | 2.237 | 2.500
Default Ring | baseline | 3.007 | 2.824 | 2.782 | 2.806 | 2.716
All values in ms. MoE traffic (Zipf s=1.2). trn1.32xlarge, 20 iters, 5 warmup.

## Slide 12: Multi-Node Benchmark (2x trn1.32xlarge, 64 ranks, EFA)
Algorithm | Type | 64KB | 256KB | 1MB | 4MB | 16MB
Agent Output | agent | 0.135 | 0.132 | 0.119 | 0.194 | 0.128
NKI AllGather | baseline | 1.071 | 1.120 | 1.149 | 1.134 | 1.168
AG+ReduceScatter | baseline | 1.097 | 1.183 | 2.062 | 1.167 | 1.196
AllGather+Slice | baseline | 2.051 | 2.103 | 2.032 | 3.557 | 3.618
Fused AllToAll | baseline | 4.131 | 2.250 | 2.220 | 2.256 | 4.293
Hierarchical | baseline | 2.547 | 4.201 | 2.473 | 4.183 | 2.354
Default Ring | baseline | 5.889 | 5.958 | 5.875 | 5.836 | 6.116
All values in ms. MoE traffic (Zipf s=1.2). 2-node EFA, 20 iters, 5 warmup.

## Slide 13: Cross-Node Penalty (2-node / single-node ratio)
Algorithm | Type | Avg Penalty | Notes
Agent Output | agent | 1.11x | Near-zero cross-node overhead
NKI AllGather | baseline | 1.28x | Moderate EFA overhead
Hierarchical | baseline | 1.34x | Topology-aware helps
AG+ReduceScatter | baseline | 1.84x | 2 dispatches amplify cross-node cost
Default Ring | baseline | 2.10x | 63 steps across EFA
Fused AllToAll | baseline | 2.21x | Significant cross-node cost
AllGather+Slice | baseline | 2.36x | Doubles with 2x data volume
Agent's all_gather + index_select scales almost perfectly across EFA.

## Slide 14: Key Observations
Latency flat from 32 KB to 16 MB
- Dispatch overhead dominates; NeuronLink/EFA never saturated
XLA op count is the only lever
- 3 ops (0.13 ms) vs 33 ops (1.05 ms) vs 93 ops (2.78 ms)
AG+ReduceScatter: 2nd-fastest intra-node (~0.73ms)
- But 2nd dispatch doubles cross-node cost (1.84x penalty)
Agent output: ~45x faster than default ring at 2 nodes
- 1 dispatch + ~3 XLA ops, 1.11x cross-node penalty

## Slide 15: What the LLM Actually Discovered
From naive_allgather seed (67 local ops)
- Round 1: 67 -> 35 ops (removes redundant slices)
- Round 2: scatter_ + index_select = 4 ops
From allgather_reduce_scatter seed
- LLM explores AG+RS pattern but can't beat 1-dispatch AG
From permute_ring seed
- Switches to AllGather pattern (86% improvement)
Agent independently arrives at all_gather + index_select
- Not shown the answer; discovers it from naive seeds

## Slide 16: Simulator vs Hardware Gap
Simulator #1: 2-gather (249 us) -> Hardware: 0.25 ms (3rd)
Simulator #2: 1-gather (493 us) -> Hardware: 0.13 ms (1st)
Simulator #4: fused (143 us) -> Hardware: 1.20 ms (5th)
Root cause
- Simulator models bandwidth and contention well
- But underweights XLA dispatch overhead
- On real hardware, dispatch cost >> link utilization
Takeaway
- Simulation prunes clearly bad candidates
- Final ranking must come from hardware measurement

## Slide 17: Lessons Learned
LLMs are search heuristics, not inventors
- Selected known patterns from prompt context
- Efficiently navigated search space
Structured feedback (CGIS) >> blind scoring
- Per-step contention diagnosis enables surgical fixes
Correctness verification is essential
- LLM-generated code fails ~30% of the time
- 5-layer verification catches subtle distributed bugs

## Slide 18: Next Steps
Improve simulator fidelity
- XLA op count as first-class cost; profile-guided calibration
- Simulator underweights dispatch overhead vs bandwidth
Reduce LLM prompt leakage
- Don't show all templates as references; force composition
End-to-end MoE training integration
- Measure wall-clock speedup, not just AllToAllV latency
Larger multi-node (4+ nodes)
- Test whether agent pattern stays optimal at higher node counts

## Slide 19: Summary
Problem: AllToAllV on Trainium is 8-23x slower than optimal
Approach: Hardware-agnostic 5-phase agent pipeline
- LLM-built simulator + evolution + HW validation + feedback loops
- 5-layer correctness verification
Result: ~0.13 ms (3 XLA ops), 1.11x cross-node penalty
- 8x vs naive AllGather, 23x vs default ring (single-node)
- ~45x faster than default ring at 2 nodes
- Drop-in module: runtime/trainium_alltoallv.py
Insight: dispatch overhead >> bandwidth at all scales tested
- Agent independently discovers optimal pattern from naive seeds